## Slide 1
BOB ON THE FLOOR
Bob on the Floor
LLM-Orchestrated Industrial Fault Response, MCP-Native
Conveyor motor anomaly -> procedure retrieval -> ladder-logic patch -> human approval
Five devices. Eight MCP tools. Zero ML dependencies.
[ 01 / 13 ]

## Slide 2
[ 02 / 13 ]
THE PROBLEM
The 2 AM Problem
Chart: Sensor drift above established baseline
| t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8
Baseline | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Vibration (mm/s) | 2 | 2.1 | 2.3 | 2.6 | 3 | 3.6 | 4.3 | 5
A conveyor motor's vibration drifts above its established baseline
No automated system connects the sensor anomaly to the maintenance procedure
An engineer must: recognise the fault pattern, search the manual, write a ladder-logic patch, and get approval — manually, under time pressure
Missed or delayed response: bearing failure, unplanned downtime, safety risk

## Slide 3
[ 03 / 13 ]
THE SOLUTION
One Pipeline. Five Stages. Fully Composable.
Bob on the Floor is a five-device fault-response pipeline exposed as discrete MCP tools. Any MCP-capable LLM orchestrator — IBM Bob, Claude, or any agent framework — can drive each stage independently or run the whole chain in a single call.
Telemetry -> Anomaly -> Procedure -> Ladder -> Approval
Schema 1 Schema 2 Schema 3 Schema 4 Schema 5
MCP tools: listen_telemetry -> detect_anomaly -> retrieve_procedure -> compile_ladder -> approve_change
Every stage is its own MCP tool — the orchestrator inspects each output before deciding whether to call the next.

## Slide 4
[ 04 / 13 ]
ARCHITECTURE
Five Devices, Five Schemas, Eight Tools
Ears
listen_telemetry
Instinct
detect_anomaly
Memory
retrieve_procedure
Hands
compile_ladder
Approval
approve_change
Schema 1
Schema 2
Schema 3
Schema 4
Schema 5
Every inter-stage boundary is enforced at runtime by jsonschema. Schema violations are hard MCP errors — not silent downstream KeyErrors.
No device imports another device's internals. If output violates the contract, the pipeline stops at that boundary with a clear error — the chain is transparent and inspectable end to end.

## Slide 5
[ 05 / 13 ]
DEVICE 1 + 2
Ears: Telemetry Ingestion | Instinct: Anomaly Detection
EARS
MCP tool: listen_telemetry
Returns Schema 1: device_id, timestamp, readings.vibration_mm_s, readings.temperature_c, readings.rpm
Pluggable source via EARS_SOURCE
fixture — cycles telemetry_stream.jsonl (default, no hardware)
modbus — live Modbus RTU via EarsModbusRtuAdapter
mqtt — stub (contribution point)
INSTINCT
MCP tool: detect_anomaly — Stateful, per-device anomaly detector. Zero ML.
Learn baseline: 100-tick rolling window (frozen once full)
Dual-threshold flag: >12% deviation and z-score >3.0
Confirm on 2 consecutive flagged ticks
Re-arm after 3 consecutive settled ticks (hysteresis)
Re-emit if severity climbs >0.10, 10-tick cooldown
vibration + temperature → bearing_wear
vibration only → vibration_drift
temperature only → thermal_creep
rpm only → other

## Slide 6
[ 06 / 13 ]
DEVICE 3
Memory: Procedure Retrieval
MCP tool: retrieve_procedure
Accepts Schema 2 (anomaly flag). Uses the description field as a free-text query. Returns Schema 3: matched procedure, source document, page number, excerpt, suggested_fix_nl, confidence score.
HOW IT WORKS
BM25Okapi index over corpus.json — 10 procedure entries from conveyor maintenance manuals, inspection tickets, and SOPs
No embedding model. No network calls at query time. Fully deterministic.
Hot-reload without restart: call reload_corpus MCP tool after uploading a new manual
EXAMPLE MATCH
Anomaly description:
"vibration rising 28% above baseline on conveyor_motor_2"
PROC-VIB-014 "Conveyor Motor Maintenance Manual" p.14
confidence: 0.91
suggested_fix_nl: "If vibration exceeds threshold, stop conveyor motor 2."

## Slide 7
[ 07 / 13 ]
DEVICE 4
Hands: NL → Ladder Logic Compiler
MCP tool: compile_ladder
Accepts Schema 3. Compiles suggested_fix_nl into a Schema 4 ladder-logic diff. No LLM — a deterministic lexer/parser/IR/codegen pipeline.
Lexer
Parser
(8 patterns)
IR
Codegen
Validator
EXAMPLE
IN: "If vibration exceeds threshold, stop conveyor motor 2."
OUT: |--[vib>THR]--(/conveyor_motor_2/)-|
validation: PASS
[PASS] program is non-empty
[PASS] every coil has contact chain

## Slide 8
[ 08 / 13 ]
DEVICE 5
Approval: Human-in-the-Loop, Four Modes
MCP tool: approve_change — mode controlled by APPROVAL_MODE env var
Mode | Behaviour
interactive | Rich terminal UI — blocks for operator input
auto_approve | Returns approved immediately — CI / known-safe fixtures
auto_reject | Returns rejected immediately — pipeline validation tests
webhook | POSTs Schema 4 to APPROVAL_WEBHOOK_URL, polls every 5s, 300s timeout
mocked interactive terminal ui
APPROVAL REQUIRED — device: conveyor_motor_2
device_id: conveyor_motor_2 dialect: IEC-61131-3
Explanation: stops conveyor motor 2 when vibration exceeds the configured threshold.
✔ program non-empty ✔ coil-contact chain
PASS
OLD RUNG
|--[vib]--( )--|
NEW RUNG
|--[vib>THR]--(/motor_2/)-|
y approve n reject skip defer ›

## Slide 9
[ 09 / 13 ]
DIFFERENTIATORS
Six Technical Differentiators
1
MCP-native pipeline composition
Five independent MCP tools. Any orchestrator can call each stage, inspect the output, and decide whether to proceed.
2
Deterministic anomaly detection, no ML
Dual-threshold (12% + z=3.0), 2-tick confirmation, 3-tick hysteresis. Fully auditable — parameters live in code.
3
NL → Ladder Logic compiler
Real lexer/parser/IR/codegen for 8 patterns. Produces valid IEC-61131-3 ASCII rungs. No LLM in the compile path.
4
Schema-enforced inter-stage contracts
jsonschema validates every MCP tool return. A violation is a hard error at the boundary, not a KeyError downstream.
5
Fully offline procedure retrieval
BM25 over a local corpus. No embedding model, no network call at query time. Hot-reloadable via reload_corpus.
6
Zero shared state via FastMCP lifespan
Every component lives in one PipelineContext, injected via lifespan. No singletons — full parallel test isolation.

## Slide 10
[ 10 / 13 ]
$ live demo
run_pipeline_tick # full pipeline in one call
listen_telemetry -> detect_anomaly -> retrieve_procedure
-> compile_ladder -> approve_change # step by step
▸ interactive approval terminal UI
▸ schema violation: hard error at the boundary

## Slide 11
[ 11 / 13 ]
UNDER THE HOOD
Tech Stack
Component | Technology
MCP server | mcp (FastMCP, stdio transport)
Anomaly detector | Pure Python — math, collections.deque
Procedure retrieval | rank_bm25, jsonschema
NL compiler | Pure Python — lexer/parser/IR/codegen
Approval UI | rich
Telemetry source | pymodbus (Modbus RTU), .jsonl fixture
Schema validation | jsonschema (all 5 schemas, every tool return)
Configuration | Environment variables or YAML (PyYAML)
Total runtime dependencies: mcp, jsonschema, rank_bm25, rich, pymodbus, PyYAML
Zero ML framework dependencies.

## Slide 12
[ 12 / 13 ]
EXTENSIBILITY
Designed to Be Extended
Add a new telemetry source
Subclass TelemetrySource, implement next_tick(), set EARS_SOURCE. Example: OPC-UA adapter, MQTT consumer.
class OpcUaSource(
TelemetrySource):
def next_tick(self):
...
EARS_SOURCE=opcua
Extend the procedure corpus
Add entries to corpus.json (or point CORPUS_PATH at a new file), call reload_corpus. No restart, no reindex command.
$ edit corpus.json
$ mcp call \
reload_corpus
# BM25 index rebuilds
# in-process
Add an NL pattern to Hands
Add a pattern function to parser.py following the existing 8-pattern structure. First match wins.
def threshold_stop(
tokens): ...
PATTERNS = [
..., new_pattern
]
Because every stage is isolated by schema contracts, extending one device never requires touching another — the schema is the only interface.

## Slide 13
[ 13 / 13 ]
SETUP
Get It Running in Two Steps
STEP 1
$ pip install -r requirements.txt
STEP 2 — add to mcp.json
{
"mcpServers": {
"bob-on-the-floor": {
"command": "python",
"args": ["/absolute/path/to/mcp_server.py"]
}
}
}
That's it.
Bob spawns the server on demand.
AVAILABLE TOOLS IMMEDIATELY
listen_telemetry retrieve_procedure run_pipeline_tick
detect_anomaly compile_ladder reload_corpus
approve_change get_pipeline_status
Repository: (add your GitHub URL here)